## Slide 1: Machine-Level Programming II: Arithmetic & Control Computer Systems 5th Lecture
ECNU
ECNU

## Slide 2: Today
ECNU
Complete addressing mode, address computation (leal)
Arithmetic operations
Control: Condition codes
Conditional branches
While loops

## Slide 3: Complete Memory Addressing Modes
ECNU
Most General Form
D(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]+ D]
  D: Constant “displacement” 1, 2, or 4 bytes
  Rb: Base register: Any of 8 integer registers
  Ri: Index register: Any, except for %esp
    Unlikely you’d use %ebp, either
  S: Scale: 1, 2, 4, or 8 (why these numbers?)
Special Cases
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D]
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]

## Slide 4: Address Computation Examples
ECNU
Expression | Address Computation | Address
0x8(%edx) | 0xf000 + 0x8 | 0xf008
(%edx,%ecx) | 0xf000 + 0x100 | 0xf100
(%edx,%ecx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%edx,2) | 2*0xf000 + 0x80 | 0x1e080
%edx | 0xf000
%ecx | 0x0100
Expression | Address Computation | Address
0x8(%edx) |  | 
(%edx,%ecx) |  | 
(%edx,%ecx,4) |  | 
0x80(,%edx,2) |  | 
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 5: Address Computation Instruction
ECNU
leal Src,Dest
  Src is address mode expression
  Set Dest to address denoted by expression
Uses
  Computing addresses without a memory reference
    E.g., translation of p = &x[i];
  Computing arithmetic expressions of the form x + k*y
    k = 1, 2, 4, or 8
Example
int mul12(int x)
{
return x*12;
}
leal (%eax,%eax,2), %eax ;t <- x+x*2
sall $2, %eax ;return t<<2
Converted to ASM by compiler:

## Slide 6: Today
ECNU
Complete addressing mode, address computation (leal)
Arithmetic operations
Control: Condition codes
Conditional branches
While loops

## Slide 7: Some Arithmetic Operations
ECNU
Two Operand Instructions:
  Format Computation
    addl Src,Dest Dest = Dest + Src
    subl Src,Dest Dest = Dest  Src
    imull Src,Dest Dest = Dest * Src
    sall Src,Dest Dest = Dest << Src Also called shll
    sarl Src,Dest Dest = Dest >> Src Arithmetic
    shrl Src,Dest Dest = Dest >> Src Logical
    xorl Src,Dest Dest = Dest ^ Src
    andl Src,Dest Dest = Dest & Src
    orl Src,Dest Dest = Dest | Src
Watch out for argument order!
No distinction between signed and unsigned int (why?)

## Slide 8: Some Arithmetic Operations
ECNU
One Operand Instructions
    incl Dest Dest = Dest + 1
    decl Dest Dest = Dest  1
    negl Dest Dest =  Dest
    notl Dest Dest = ~Dest
See book for more instructions

## Slide 9: Arithmetic Expression Example
ECNU
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x+4;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 * t5;
return rval;
}
arith:
pushl %ebp
movl %esp, %ebp
movl 8(%ebp), %ecx
movl 12(%ebp), %edx
leal (%edx,%edx,2), %eax
sall $4, %eax
leal 4(%ecx,%eax), %eax
addl %ecx, %edx
addl 16(%ebp), %edx
imull %edx, %eax
popl %ebp
ret
Body
Set
Up
Finish

## Slide 10: Understanding arith
 | •
 | •
 | •
16 | z
12 | y
8 | x
4 | Rtn Addr
0 | Old %ebp
ECNU
movl 8(%ebp), %ecx
movl 12(%ebp), %edx
leal (%edx,%edx,2), %eax
sall $4, %eax
leal 4(%ecx,%eax), %eax
addl %ecx, %edx
addl 16(%ebp), %edx
imull %edx, %eax
%ebp
Offset
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x+4;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 * t5;
return rval;
}

## Slide 11: Understanding arith
 | •
 | •
 | •
16 | z
12 | y
8 | x
4 | Rtn Addr
0 | Old %ebp
ECNU
%ebp
Offset
Stack
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x+4;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 * t5;
return rval;
}
movl 8(%ebp), %ecx # ecx = x
movl 12(%ebp), %edx # edx = y
leal (%edx,%edx,2), %eax # eax = y*3
sall $4, %eax # eax *= 16 (t4)
leal 4(%ecx,%eax), %eax # eax = t4 +x+4 (t5)
addl %ecx, %edx # edx = x+y (t1)
addl 16(%ebp), %edx # edx += z (t2)
imull %edx, %eax # eax = t2 * t5 (rval)

## Slide 12: Observations about arith
ECNU
  Instructions in different order from C code
  Some expressions require multiple instructions
  Some instructions cover multiple expressions
  Get exact same code when compile:
  (x+y+z)*(x+4+48*y)
movl 8(%ebp), %ecx # ecx = x
movl 12(%ebp), %edx # edx = y
leal (%edx,%edx,2), %eax # eax = y*3
sall $4, %eax # eax *= 16 (t4)
leal 4(%ecx,%eax), %eax # eax = t4 +x+4 (t5)
addl %ecx, %edx # edx = x+y (t1)
addl 16(%ebp), %edx # edx += z (t2)
imull %edx, %eax # eax = t2 * t5 (rval)
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x+4;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 * t5;
return rval;
}

## Slide 13: Another Example
ECNU
int logical(int x, int y)
{
int t1 = x^y;
int t2 = t1 >> 17;
int mask = (1<<13) - 7;
int rval = t2 & mask;
return rval;
}
logical:
pushl %ebp
movl %esp,%ebp
movl 12(%ebp),%eax
xorl 8(%ebp),%eax
sarl $17,%eax
andl $8185,%eax
popl %ebp
ret
Body
Set
Up
Finish
movl 12(%ebp),%eax # eax = y
xorl 8(%ebp),%eax # eax = x^y (t1)
sarl $17,%eax # eax = t1>>17 (t2)
andl $8185,%eax # eax = t2 & mask (rval)

## Slide 14: Another Example
ECNU
int logical(int x, int y)
{
int t1 = x^y;
int t2 = t1 >> 17;
int mask = (1<<13) - 7;
int rval = t2 & mask;
return rval;
}
logical:
pushl %ebp
movl %esp,%ebp
movl 12(%ebp),%eax
xorl 8(%ebp),%eax
sarl $17,%eax
andl $8185,%eax
popl %ebp
ret
Body
Set
Up
Finish
movl 12(%ebp),%eax # eax = y
xorl 8(%ebp),%eax # eax = x^y (t1)
sarl $17,%eax # eax = t1>>17 (t2)
andl $8185,%eax # eax = t2 & mask (rval)

## Slide 15: Another Example
ECNU
int logical(int x, int y)
{
int t1 = x^y;
int t2 = t1 >> 17;
int mask = (1<<13) - 7;
int rval = t2 & mask;
return rval;
}
logical:
pushl %ebp
movl %esp,%ebp
movl 12(%ebp),%eax
xorl 8(%ebp),%eax
sarl $17,%eax
andl $8185,%eax
popl %ebp
ret
Body
Set
Up
Finish
movl 12(%ebp),%eax # eax = y
xorl 8(%ebp),%eax # eax = x^y (t1)
sarl $17,%eax # eax = t1>>17 (t2)
andl $8185,%eax # eax = t2 & mask (rval)

## Slide 16: Another Example
ECNU
int logical(int x, int y)
{
int t1 = x^y;
int t2 = t1 >> 17;
int mask = (1<<13) - 7;
int rval = t2 & mask;
return rval;
}
logical:
pushl %ebp
movl %esp,%ebp
movl 12(%ebp),%eax
xorl 8(%ebp),%eax
sarl $17,%eax
andl $8185,%eax
popl %ebp
ret
Body
Set
Up
Finish
movl 12(%ebp),%eax # eax = y
xorl 8(%ebp),%eax # eax = x^y (t1)
sarl $17,%eax # eax = t1>>17 (t2)
andl $8185,%eax # eax = t2 & mask (rval)
213 = 8192, 213 – 7 = 8185

## Slide 17: Today
ECNU
Complete addressing mode, address computation (leal)
Arithmetic operations
Control: Condition codes
Conditional branches
Loops

## Slide 18: Processor State (IA32, Partial)
ECNU
Information about currently executing program
  Temporary data ( %eax, … )
  Location of runtime stack ( %ebp,%esp )
  Location of current code control point ( %eip, … )
  Status of recent tests ( CF, ZF, SF, OF )
%eip
General purpose
registers
Current stack top
Current stack frame
Instruction pointer
CF
ZF
SF
OF
Condition codes
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp

## Slide 19: Condition Codes (Implicit Setting)
ECNU
Single bit registers
  CF Carry Flag (for unsigned) SF Sign Flag (for signed)
  ZF Zero Flag OF Overflow Flag (for signed)
Implicitly set (think of it as side effect) by arithmetic operations
  Example: addl/addq Src,Dest ↔ t = a+b
  CF set if carry out from most significant bit (unsigned overflow)
  ZF set if t == 0
  SF set if t < 0 (as signed)
  OF set if two’s-complement (signed) overflow (a>0 && b>0 && t<0) || (a<0 && b<0 && t>=0)
Not set by leal instruction
Full documentation (IA32)

## Slide 20: Condition Codes (Explicit Setting: Compare)
ECNU
Explicit Setting by Compare Instruction
  cmpl/cmpq Src2, Src1
  cmpl b,a like computing a-b without setting destination
  CF set if carry out from most significant bit (used for unsigned comparisons)
  ZF set if a == b
  SF set if (a-b) < 0 (as signed)
  OF set if two’s-complement (signed) overflow (a>0 && b<0 && (a-b)<0) || (a<0 && b>0 && (a-b)>0)

## Slide 21: Condition Codes (Explicit Setting: Test)
ECNU
Explicit Setting by Test instruction
  testl/testq Src2, Src1 testl b,a like computing a&b without setting destination
  Sets condition codes based on value of Src1 & Src2
  Useful to have one of the operands be a mask
  ZF set when a&b == 0
  SF set when a&b < 0

## Slide 22: Reading Condition Codes
ECNU
SetX Instructions
  Set single byte based on combinations of condition codes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (Signed)
setge | ~(SF^OF) | Greater or Equal (Signed)
setl | (SF^OF) | Less (Signed)
setle | (SF^OF)¦ZF | Less or Equal (Signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)

## Slide 23: Reading Condition Codes (Cont.)
movl 12(%ebp),%eax # eax = y
cmpl %eax,8(%ebp) # Compare x : y
setg %al # al = x > y
movzbl %al,%eax # Zero rest of %eax
ECNU
SetX Instructions:
  Set single byte based on combination of condition codes
One of 8 addressable byte registers
  Does not alter remaining 3 bytes
  Typically use movzbl to finish job
int gt (int x, int y)
{
return x > y;
}
Body
%eax | %ah | %al
%ecx | %ch | %cl
%edx | %dh | %dl
%ebx | %bh | %bl
%esi |  | 
%edi |  | 
%esp |  | 
%ebp |  | 

## Slide 24: Reading Condition Codes: x86-64
ECNU
int gt (long x, long y)
{
return x > y;
}
cmpl %esi, %edi
setg %al
movzbl %al, %eax
Bodies
long lgt (long x, long y)
{
return x > y;
}
SetX Instructions:
  Set single byte based on combination of condition codes
  Does not alter remaining 3 bytes
Is %rax zero?
Yes: 32-bit instructions set high order 32 bits to 0!
cmpq %rsi, %rdi
setg %al
movzbl %al, %eax

## Slide 25: Today
ECNU
Complete addressing mode, address computation (leal)
Arithmetic operations
x86-64
Control: Condition codes
Conditional branches & Moves
Loops

## Slide 26: Jumping
ECNU
jX Instructions
  Jump to different part of code depending on condition codes
jX | Condition | Description
jmp | 1 | Unconditional
je | ZF | Equal / Zero
jne | ~ZF | Not Equal / Not Zero
js | SF | Negative
jns | ~SF | Nonnegative
jg | ~(SF^OF)&~ZF | Greater (Signed)
jge | ~(SF^OF) | Greater or Equal (Signed)
jl | (SF^OF) | Less (Signed)
jle | (SF^OF)¦ZF | Less or Equal (Signed)
ja | ~CF&~ZF | Above (unsigned)
jb | CF | Below (unsigned)

## Slide 27: Conditional Branch Example
ECNU
int absdiff(int x, int y)
{
int result;
if (x > y) {
result = x-y;
} else {
result = y-x;
}
return result;
}
absdiff:
pushl %ebp
movl %esp, %ebp
movl 8(%ebp), %edx
movl 12(%ebp), %eax
cmpl %eax, %edx
jle .L6
subl %eax, %edx
movl %edx, %eax
jmp .L7
.L6:
subl %edx, %eax
.L7:
popl %ebp
ret
Body1
Setup
Finish
Body2b
Body2a

## Slide 28: Conditional Branch Example (Cont.)
ECNU
int goto_ad(int x, int y)
{
int result;
if (x <= y) goto Else;
result = x-y;
goto Exit;
Else:
result = y-x;
Exit:
return result;
}
C allows “goto” as means of transferring control
  Closer to machine-level programming style
Generally considered bad coding style
absdiff:
pushl %ebp
movl %esp, %ebp
movl 8(%ebp), %edx
movl 12(%ebp), %eax
cmpl %eax, %edx
jle .L6
subl %eax, %edx
movl %edx, %eax
jmp .L7
.L6:
subl %edx, %eax
.L7:
popl %ebp
ret
Body1
Setup
Finish
Body2b
Body2a

## Slide 29: Conditional Branch Example (Cont.)
ECNU
int goto_ad(int x, int y)
{
int result;
if (x <= y) goto Else;
result = x-y;
goto Exit;
Else:
result = y-x;
Exit:
return result;
}
absdiff:
pushl %ebp
movl %esp, %ebp
movl 8(%ebp), %edx
movl 12(%ebp), %eax
cmpl %eax, %edx
jle .L6
subl %eax, %edx
movl %edx, %eax
jmp .L7
.L6:
subl %edx, %eax
.L7:
popl %ebp
ret
Body1
Setup
Finish
Body2b
Body2a

## Slide 30: Conditional Branch Example (Cont.)
ECNU
int goto_ad(int x, int y)
{
int result;
if (x <= y) goto Else;
result = x-y;
goto Exit;
Else:
result = y-x;
Exit:
return result;
}
absdiff:
pushl %ebp
movl %esp, %ebp
movl 8(%ebp), %edx
movl 12(%ebp), %eax
cmpl %eax, %edx
jle .L6
subl %eax, %edx
movl %edx, %eax
jmp .L7
.L6:
subl %edx, %eax
.L7:
popl %ebp
ret
Body1
Setup
Finish
Body2b
Body2a

## Slide 31: Conditional Branch Example (Cont.)
ECNU
int goto_ad(int x, int y)
{
int result;
if (x <= y) goto Else;
result = x-y;
goto Exit;
Else:
result = y-x;
Exit:
return result;
}
absdiff:
pushl %ebp
movl %esp, %ebp
movl 8(%ebp), %edx
movl 12(%ebp), %eax
cmpl %eax, %edx
jle .L6
subl %eax, %edx
movl %edx, %eax
jmp .L7
.L6:
subl %edx, %eax
.L7:
popl %ebp
ret
Body1
Setup
Finish
Body2b
Body2a

## Slide 32: General Conditional Expression Translation
ECNU
C Code
val = Test ? Then_Expr : Else_Expr;
Goto Version
nt = !Test;
if (nt) goto Else;
val = Then_Expr;
goto Done;
Else:
val = Else_Expr;
Done:
. . .
  Test is expression returning integer
    = 0 interpreted as false
    ≠ 0 interpreted as true
  Create separate code regions for then & else expressions
  Execute appropriate one
val = x>y ? x-y : y-x;

## Slide 33: Using Conditional Moves
ECNU
C Code
val = Test
? Then_Expr
: Else_Expr;
Goto Version
tval = Then_Expr;
result = Else_Expr;
t = Test;
if (t) result = tval;
return result;
Conditional Move Instructions
  Instruction supports:
    if (Test) Dest  Src
  Supported in post-1995 x86 processors
  GCC does not always use them
    Wants to preserve compatibility with ancient processors
    Enabled for x86-64
    Use switch –march=i686 for IA32
Why?
  Branches are very disruptive to instruction flow through pipelines
  Conditional move do not require control transfer

## Slide 34: Conditional Move Example: x86-64
ECNU
int absdiff(int x, int y) {
int result;
if (x > y) {
result = x-y;
} else {
result = y-x;
}
return result;
}
absdiff:
movl %edi, %edx
subl %esi, %edx # tval = x-y
movl %esi, %eax
subl %edi, %eax # result = y-x
cmpl %esi, %edi # Compare x:y
cmovg %edx, %eax # If >, result = tval
ret
x in %edi
y in %esi

## Slide 35: Bad Cases for Conditional Move
ECNU
Expensive Computations
Both values get computed
Only makes sense when computations are very simple
val = Test(x) ? Hard1(x) : Hard2(x);
Risky Computations
Both values get computed
May have undesirable effects
val = p ? *p : 0;
Computations with side effects
Both values get computed
Must be side-effect free
val = x > 0 ? x*=7 : x+=3;

## Slide 36: Today
ECNU
Complete addressing mode, address computation (leal)
Arithmetic operations
x86-64
Control: Condition codes
Conditional branches and moves
Loops

## Slide 37: “Do-While” Loop Example
ECNU
C Code
int pcount_do(unsigned x) {
int result = 0;
do {
result += x & 0x1;
x >>= 1;
} while (x);
return result;
}
Goto Version
int pcount_do(unsigned x)
{
int result = 0;
loop:
result += x & 0x1;
x >>= 1;
if (x)
goto loop;
return result;
}
Count number of 1’s in argument x (“popcount”)
Use conditional branch to either continue looping or to exit loop

## Slide 38: “Do-While” Loop Compilation
ECNU
Goto Version
Registers:
  %edx x
  %ecx result
movl $0, %ecx # result = 0
.L2: # loop:
movl %edx, %eax
andl $1, %eax # t = x & 1
addl %eax, %ecx # result += t
shrl %edx # x >>= 1
jne .L2 # If !0, goto loop
int pcount_do(unsigned x) {
int result = 0;
loop:
result += x & 0x1;
x >>= 1;
if (x)
goto loop;
return result;
}

## Slide 39: General “Do-While” Translation
ECNU
C Code
do
Body
while (Test);
Goto Version
loop:
Body
if (Test)
goto loop
Body:
Test returns integer
  = 0 interpreted as false
  ≠ 0 interpreted as true
{
Statement1;
Statement2;
…
Statementn;
}

## Slide 40: “While” Loop Example
ECNU
C Code
Goto Version
Is this code equivalent to the do-while version?
  Must jump out of loop if test fails
int pcount_while(unsigned x) {
int result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
int pcount_do(unsigned x) {
int result = 0;
if (!x) goto done;
loop:
result += x & 0x1;
x >>= 1;
if (x)
goto loop;
done:
return result;
}

## Slide 41: General “While” Translation
ECNU
While version
while (Test)
Body
Do-While Version
if (!Test)
goto done;
do
Body
while(Test);
done:
Goto Version
if (!Test)
goto done;
loop:
Body
if (Test)
goto loop;
done:

## Slide 42: “For” Loop Example
ECNU
C Code
Is this code equivalent to other versions?
#define WSIZE 8*sizeof(int)
int pcount_for(unsigned x) {
int i;
int result = 0;
for (i = 0; i < WSIZE; i++) {
unsigned mask = 1 << i;
result += (x & mask) != 0;
}
return result;
}

## Slide 43: “For” Loop Form
ECNU
for (Init; Test; Update )
Body
General Form
for (i = 0; i < WSIZE; i++) {
unsigned mask = 1 << i;
result += (x & mask) != 0;
}
i = 0
i < WSIZE
i++
{
unsigned mask = 1 << i;
result += (x & mask) != 0;
}
Init
Test
Update
Body

## Slide 44: “For” Loop  While Loop
ECNU
for (Init; Test; Update )
Body
For Version
Init;
while (Test ) {
Body
Update;
}
While Version

## Slide 45: “For” Loop  …  Goto
ECNU
for (Init; Test; Update )
Body
For Version
Init;
while (Test ) {
Body
Update;
}
While Version
Init;
if (!Test)
goto done;
do
Body
Update
while(Test);
done:
Init;
if (!Test)
goto done;
loop:
Body
Update
if (Test)
goto loop;
done:

## Slide 46: “For” Loop Conversion Example
ECNU
C Code
Initial test can be optimized away
#define WSIZE 8*sizeof(int)
int pcount_for(unsigned x) {
int i;
int result = 0;
for (i = 0; i < WSIZE; i++) {
unsigned mask = 1 << i;
result += (x & mask) != 0;
}
return result;
}
Goto Version
int pcount_for_gt(unsigned x) {
int i;
int result = 0;
i = 0;
if (!(i < WSIZE))
goto done;
loop:
{
unsigned mask = 1 << i;
result += (x & mask) != 0;
}
i++;
if (i < WSIZE)
goto loop;
done:
return result;
}
Init
!Test
Body
Update
Test

## Slide 47: Summary
ECNU
Today
  Complete addressing mode, address computation (leal)
  Arithmetic operations
  Control: Condition codes
  Conditional branches & conditional moves
  Loops
Next Time
  Switch statements
  Stack
  Call / return
  Procedure call discipline