## Slide 1: Machine-Level Programming III: Switch Statements and IA32 Procedures Computer Systems 6th Lecture
ECNU

## Slide 2: Today
ECNU
Switch statements
IA 32 Procedures
  Stack Structure
  Calling Conventions
  Illustrations of Recursion & Pointers

## Slide 3: Switch Statement Example
ECNU
Multiple case labels
  Here: 5 & 6
Fall through cases
  Here: 2
Missing cases
  Here: 4
long switch_eg
(long x, long y, long z)
{
long w = 1;
switch(x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
}
return w;
}

## Slide 4: Jump Table Structure
ECNU
Code Block
0
Targ0:
Code Block
1
Targ1:
Code Block
2
Targ2:
Code Block
n–1
Targn-1:
•
•
•
Targ0
Targ1
Targ2
Targn-1
•
•
•
jtab:
target = JTab[x];
goto *target;
switch(x) {
case val_0:
Block 0
case val_1:
Block 1
• • •
case val_n-1:
Block n–1
}
Switch Form
Approximate Translation
Jump Table
Jump Targets

## Slide 5: Switch Statement Example (IA32)
ECNU
Setup:
long switch_eg(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
switch_eg:
pushl %ebp # Setup
movl %esp, %ebp # Setup
movl 8(%ebp), %eax # %eax = x
cmpl $6, %eax # Compare x:6
ja .L2 # If unsigned > goto default
jmp *.L7(,%eax,4) # Goto *JTab[x]
What range of values takes default?
Note that w not initialized here

## Slide 6: Switch Statement Example (IA32)
ECNU
long switch_eg(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
Indirect jump
Jump table
.section .rodata
.align 4
.L7:
.long .L2 # x = 0
.long .L3 # x = 1
.long .L4 # x = 2
.long .L5 # x = 3
.long .L2 # x = 4
.long .L6 # x = 5
.long .L6 # x = 6
Setup:
switch_eg:
pushl %ebp # Setup
movl %esp, %ebp # Setup
movl 8(%ebp), %eax # eax = x
cmpl $6, %eax # Compare x:6
ja .L2 # If unsigned > goto default
jmp *.L7(,%eax,4) # Goto *JTab[x]

## Slide 7: Assembly Setup Explanation
ECNU
Table Structure
  Each target requires 4 bytes
  Base address at .L7
Jumping
  Direct: jmp .L2
  Jump target is denoted by label .L2
  Indirect: jmp *.L7(,%eax,4)
  Start of jump table: .L7
  Must scale by factor of 4 (labels have 32-bits = 4 Bytes on IA32)
  Fetch target from effective Address .L7 + eax*4
    Only for 0 ≤ x ≤ 6
Jump table
.section .rodata
.align 4
.L7:
.long .L2 # x = 0
.long .L3 # x = 1
.long .L4 # x = 2
.long .L5 # x = 3
.long .L2 # x = 4
.long .L6 # x = 5
.long .L6 # x = 6

## Slide 8: Jump Table
.section .rodata
.align 4
.L7:
.long .L2 # x = 0
.long .L3 # x = 1
.long .L4 # x = 2
.long .L5 # x = 3
.long .L2 # x = 4
.long .L6 # x = 5
.long .L6 # x = 6
ECNU
Jump table
switch(x) {
case 1: // .L3
w = y*z;
break;
case 2: // .L4
w = y/z;
/* Fall Through */
case 3: // .L5
w += z;
break;
case 5:
case 6: // .L6
w -= z;
break;
default: // .L2
w = 2;
}

## Slide 9: Handling Fall-Through
ECNU
long w = 1;
. . .
switch(x) {
. . .
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
. . .
}
case 3:
w = 1;
goto merge;
case 2:
w = y/z;
merge:
w += z;

## Slide 10: Code Blocks (Partial)
ECNU
.L2: # Default
movl $2, %eax # w = 2
jmp .L8 # Goto done
.L5: # x == 3
movl $1, %eax # w = 1
jmp .L9 # Goto merge
.L3: # x == 1
movl 16(%ebp), %eax # z
imull 12(%ebp), %eax # w = y*z
jmp .L8 # Goto done
switch(x) {
case 1: // .L3
w = y*z;
break;
. . .
case 3: // .L5
w += z;
break;
. . .
default: // .L2
w = 2;
}

## Slide 11: Code Blocks (Rest)
ECNU
.L4: # x == 2
movl 12(%ebp), %edx
movl %edx, %eax
sarl $31, %edx
idivl 16(%ebp) # w = y/z
.L9: # merge:
addl 16(%ebp), %eax # w += z
jmp .L8 # goto done
.L6: # x == 5, 6
movl $1, %eax # w = 1
subl 16(%ebp), %eax # w = 1-z
switch(x) {
. . .
case 2: // .L4
w = y/z;
/* Fall Through */
merge: // .L9
w += z;
break;
case 5:
case 6: // .L6
w -= z;
break;
}

## Slide 12: Switch Code (Finish)
ECNU
Noteworthy Features
  Jump table avoids sequencing through cases
    Constant time, rather than linear
  Use jump table to handle holes and duplicate tags
  Use program sequencing to handle fall-through
  Don’t initialize w = 1 unless really need it
return w;
.L8: # done:
popl %ebp
ret

## Slide 13: x86-64 Switch Implementation
ECNU
.section .rodata
.align 8
.L7:
.quad .L2 # x = 0
.quad .L3 # x = 1
.quad .L4 # x = 2
.quad .L5 # x = 3
.quad .L2 # x = 4
.quad .L6 # X = 5
.quad .L6 # x = 6
Jump Table
Same general idea, adapted to 64-bit code
Table entries 64 bits (pointers)
Cases use revised code
.L3:
movq %rdx, %rax
imulq %rsi, %rax
ret
switch(x) {
case 1: // .L3
w = y*z;
break;
. . .
}

## Slide 14: IA32 Object Code
ECNU
Setup
  Label .L2 becomes address 0x8048422
  Label .L7 becomes address 0x8048660
08048410 <switch_eg>:
. . .
8048419: 77 07 ja 8048422 <switch_eg+0x12>
804841b: ff 24 85 60 86 04 08 jmp *0x8048660(,%eax,4)
switch_eg:
. . .
ja .L2 # If unsigned > goto default
jmp *.L7(,%eax,4) # Goto *JTab[x]
Assembly Code
Disassembled Object Code

## Slide 15: IA32 Object Code (cont.)
ECNU
Jump Table
  Doesn’t show up in disassembled code
  Can inspect using GDB
  gdb switch
  (gdb) x/7xw 0x8048660
    Examine 7 hexadecimal format “words” (4-bytes each)
    Use command “help x” to get format documentation
0x8048660: 0x08048422 0x08048432 0x0804843b 0x08048429
0x8048670: 0x08048422 0x0804844b 0x0804844b

## Slide 16: IA32 Object Code (cont.)
ECNU
Deciphering Jump Table
0x8048660: 0x08048422 0x08048432 0x0804843b 0x08048429
0x8048670: 0x08048422 0x0804844b 0x0804844b
Address | Value | x
0x8048660 | 0x8048422 | 0
0x8048664 | 0x8048432 | 1
0x8048668 | 0x804843b | 2
0x804866c | 0x8048429 | 3
0x8048670 | 0x8048422 | 4
0x8048674 | 0x804844b | 5
0x8048678 | 0x804844b | 6

## Slide 17: Disassembled Targets
ECNU
8048422: b8 02 00 00 00 mov $0x2,%eax
8048427: eb 2a jmp 8048453 <switch_eg+0x43>
8048429: b8 01 00 00 00 mov $0x1,%eax
804842e: 66 90 xchg %ax,%ax # noop
8048430: eb 14 jmp 8048446 <switch_eg+0x36>
8048432: 8b 45 10 mov 0x10(%ebp),%eax
8048435: 0f af 45 0c imul 0xc(%ebp),%eax
8048439: eb 18 jmp 8048453 <switch_eg+0x43>
804843b: 8b 55 0c mov 0xc(%ebp),%edx
804843e: 89 d0 mov %edx,%eax
8048440: c1 fa 1f sar $0x1f,%edx
8048443: f7 7d 10 idivl 0x10(%ebp)
8048446: 03 45 10 add 0x10(%ebp),%eax
8048449: eb 08 jmp 8048453 <switch_eg+0x43>
804844b: b8 01 00 00 00 mov $0x1,%eax
8048450: 2b 45 10 sub 0x10(%ebp),%eax
8048453: 5d pop %ebp
8048454: c3 ret

## Slide 18: Matching Disassembled Targets
ECNU
8048422: mov $0x2,%eax
8048427: jmp 8048453 <switch_eg+0x43>
8048429: mov $0x1,%eax
804842e: xchg %ax,%ax
8048430: jmp 8048446 <switch_eg+0x36>
8048432: mov 0x10(%ebp),%eax
8048435: imul 0xc(%ebp),%eax
8048439: jmp 8048453 <switch_eg+0x43>
804843b: mov 0xc(%ebp),%edx
804843e: mov %edx,%eax
8048440: sar $0x1f,%edx
8048443: idivl 0x10(%ebp)
8048446: add 0x10(%ebp),%eax
8048449: jmp 8048453 <switch_eg+0x43>
804844b: mov $0x1,%eax
8048450: sub 0x10(%ebp),%eax
8048453: pop %ebp
8048454: ret
Value
0x8048422
0x8048432
0x804843b
0x8048429
0x8048422
0x804844b
0x804844b

## Slide 19: Summarizing
ECNU
C Control
  if-then-else
  do-while
  while, for
  switch
Assembler Control
  Conditional jump
  Conditional move
  Indirect jump
  Compiler generates code sequence to implement more complex control
Standard Techniques
  Loops converted to do-while form
  Large switch statements use jump tables
  Sparse switch statements may use decision trees

## Slide 20: Today
ECNU
Switch statements
IA 32 Procedures
  Stack Structure
  Calling Conventions
  Illustrations of Recursion & Pointers

## Slide 21: IA32 Stack
ECNU
Region of memory managed with stack discipline
Grows toward lower addresses
Register %esp contains lowest stack address
  address of “top” element
Stack Pointer: %esp
Stack Grows
Down
Increasing
Addresses
Stack “Top”
Stack “Bottom”

## Slide 22: IA32 Stack: Push
ECNU
pushl Src
  Fetch operand at Src
  Decrement %esp by 4
  Write operand at address given by %esp
-4
Stack Grows
Down
Increasing
Addresses
Stack “Bottom”
Stack Pointer: %esp
Stack “Top”

## Slide 23: IA32 Stack: Pop
Stack Pointer: %esp
Stack Grows
Down
Increasing
Addresses
Stack “Top”
Stack “Bottom”
ECNU
+4

## Slide 24: Procedure Control Flow
ECNU
Use stack to support procedure call and return
Procedure call: call label
  Push return address on stack
  Jump to label
Return address:
  Address of the next instruction right after call
  Example from disassembly
  804854e: e8 3d 06 00 00 call 8048b90 <main>
  8048553: 50 pushl %eax
  Return address = 0x8048553
Procedure return: ret
  Pop address from stack
  Jump to address

## Slide 25: Procedure Call Example
0x8048553
0x104
ECNU
%esp
%eip
%esp
%eip
0x8048b90
0x108
0x10c
0x110
0x104
0x804854e
123
0x108
0x10c
0x110
123
0x108
call 8048b90
804854e: e8 3d 06 00 00 call 8048b90 <main>
8048553: 50 pushl %eax
%eip: program counter

## Slide 26: Procedure Return Example
ECNU
%esp
%eip
0x104
%esp
%eip
0x8048591
0x104
0x108
0x10c
0x110
0x8048553
123
0x108
0x10c
0x110
123
ret
8048591: c3 ret
0x108
0x8048553
0x8048553
%eip: program counter

## Slide 27: Stack-Based Languages
ECNU
Languages that support recursion
  e.g., C, Pascal, Java
  Code must be “Reentrant”
    Multiple simultaneous instantiations of single procedure
  Need some place to store state of each instantiation
    Arguments
    Local variables
    Return pointer
Stack discipline
  State for given procedure needed for limited time
    From when called to when return
  Callee returns before caller does
Stack allocated in Frames
  state for single procedure instantiation

## Slide 28: Call Chain Example
ECNU
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
yoo
who
amI
amI
amI
Example
Call Chain
amI
Procedure amI() is recursive

## Slide 29: Stack Frames
ECNU
Frame Pointer: %ebp
Contents
  Local variables
  Return information
  Temporary space
Management
  Space allocated when enter procedure
    “Set-up” code
  Deallocated when return
    “Finish” code
Stack Pointer: %esp
Stack “Top”
Previous Frame
Frame for proc

## Slide 30: Example
ECNU
yoo
who
amI
amI
amI
amI
yoo
%ebp
%esp
Stack
yoo
yoo(…)
{
•
•
who();
•
•
}

## Slide 31: Example
yoo(…)
{
•
•
who();
•
•
}
ECNU
yoo
who
amI
amI
amI
amI
yoo
%ebp
%esp
Stack
yoo
who
who(…)
{
• • •
amI();
• • •
amI();
• • •
}

## Slide 32: Example
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
ECNU
yoo
who
amI
amI
amI
amI
yoo
%ebp
%esp
Stack
yoo
who
amI
amI(…)
{
•
•
amI();
•
•
}

## Slide 33: Example
ECNU
yoo
who
amI
amI
amI
amI
yoo
%ebp
%esp
Stack
yoo
who
amI
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 34: Example
ECNU
yoo
who
amI
amI
amI
amI
yoo
%ebp
%esp
Stack
yoo
who
amI
amI
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 35: Example
ECNU
yoo
who
amI
amI
amI
amI
yoo
%ebp
%esp
Stack
yoo
who
amI
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 36: Example
ECNU
yoo
who
amI
amI
amI
amI
yoo
%ebp
%esp
Stack
yoo
who
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 37: Example
ECNU
yoo
who
amI
amI
amI
amI
yoo
%ebp
%esp
Stack
yoo
who
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}

## Slide 38: Example
ECNU
yoo
who
amI
amI
amI
amI
yoo
%ebp
%esp
Stack
yoo
who
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 39: Example
ECNU
yoo
who
amI
amI
amI
amI
yoo
%ebp
%esp
Stack
yoo
who
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}

## Slide 40: Example
ECNU
yoo
who
amI
amI
amI
amI
yoo
%ebp
%esp
Stack
yoo
yoo(…)
{
•
•
who();
•
•
}

## Slide 41: IA32/Linux Stack Frame
ECNU
Current Stack Frame (“Top” to Bottom)
  “Argument build:” Parameters for function about to call
  Local variables If can’t keep in registers
  Saved register context
  Old frame pointer
Caller Stack Frame
  Return address
    Pushed by call instruction
  Arguments for this call
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
Old %ebp
Arguments
Caller
Frame
Frame pointer %ebp
Stack pointer
%esp

## Slide 42: Revisiting swap
ECNU
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
int course1 = 15213;
int course2 = 18243;
void call_swap() {
swap(&course1, &course2);
}
call_swap:
• • •
subl $8, %esp
movl $course2, 4(%esp)
movl $course1, (%esp)
call swap
• • •
&course2
&course1
Rtn adr
%esp
Resulting
Stack
•
•
•
Calling swap from call_swap
%esp
%esp
subl
call

## Slide 43: Revisiting swap
ECNU
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
pushl %ebp
movl %esp, %ebp
pushl %ebx
movl 8(%ebp), %edx
movl 12(%ebp), %ecx
movl (%edx), %ebx
movl (%ecx), %eax
movl %eax, (%edx)
movl %ebx, (%ecx)
popl %ebx
popl %ebp
ret
Body
Set
Up
Finish

## Slide 44: swap Setup #1
ECNU
swap:
pushl %ebp
movl %esp,%ebp
pushl %ebx
Resulting Stack
&course2
&course1
Rtn adr
%esp
Entering Stack
•
•
•
%ebp
yp
xp
Rtn adr
Old %ebp
%ebp
•
•
•
%esp

## Slide 45: swap Setup #2
ECNU
swap:
pushl %ebp
movl %esp,%ebp
pushl %ebx
Resulting Stack
&course2
&course1
Rtn adr
%esp
Entering Stack
•
•
•
%ebp
yp
xp
Rtn adr
Old %ebp
%ebp
•
•
•
%esp

## Slide 46: swap Setup #3
ECNU
swap:
pushl %ebp
movl %esp,%ebp
pushl %ebx
Resulting Stack
&course2
&course1
Rtn adr
%esp
Entering Stack
•
•
•
%ebp
yp
xp
Rtn adr
Old %ebp
%ebp
•
•
•
%esp
Old %ebx

## Slide 47: swap Body
ECNU
movl 8(%ebp),%edx # get xp
movl 12(%ebp),%ecx # get yp
. . .
Resulting Stack
&course2
&course1
Rtn adr
%esp
Entering Stack
•
•
•
%ebp
yp
xp
Rtn adr
Old %ebp
%ebp
•
•
•
%esp
Old %ebx
Offset relative to %ebp
12
8
4

## Slide 48: swap Finish
ECNU
Stack Before Finish
popl %ebx
popl %ebp
yp
xp
Rtn adr
Old %ebp
%ebp
•
•
•
%esp
Old %ebx
Resulting Stack
yp
xp
Rtn adr
•
•
•
%ebp
%esp
Observation
  Saved and restored register %ebx
  Not so for %eax, %ecx, %edx

## Slide 49: Disassembled swap
ECNU
08048384 <swap>:
8048384: 55 push %ebp
8048385: 89 e5 mov %esp,%ebp
8048387: 53 push %ebx
8048388: 8b 55 08 mov 0x8(%ebp),%edx
804838b: 8b 4d 0c mov 0xc(%ebp),%ecx
804838e: 8b 1a mov (%edx),%ebx
8048390: 8b 01 mov (%ecx),%eax
8048392: 89 02 mov %eax,(%edx)
8048394: 89 19 mov %ebx,(%ecx)
8048396: 5b pop %ebx
8048397: 5d pop %ebp
8048398: c3 ret
80483b4: movl $0x8049658,0x4(%esp) # Copy &course2
80483bc: movl $0x8049654,(%esp) # Copy &course1
80483c3: call 8048384 <swap> # Call swap
80483c8: leave # Prepare to return
80483c9: ret # Return
Calling Code

## Slide 50: Today
ECNU
Switch statements
IA 32 Procedures
  Stack Structure
  Calling Conventions
  Illustrations of Recursion & Pointers

## Slide 51: Register Saving Conventions
ECNU
When procedure yoo calls who:
  yoo is the caller
  who is the callee
Can register be used for temporary storage?
  Contents of register %edx overwritten by who
  This could be trouble ➙ something should be done!
    Need some coordination
yoo:
• • •
movl $15213, %edx
call who
addl %edx, %eax
• • •
ret
who:
• • •
movl 8(%ebp), %edx
addl $18243, %edx
• • •
ret

## Slide 52: Register Saving Conventions
ECNU
When procedure yoo calls who:
  yoo is the caller
  who is the callee
Can register be used for temporary storage?
Conventions
  “Caller Save”
    Caller saves temporary values in its frame before the call
  “Callee Save”
    Callee saves temporary values in its frame before using

## Slide 53: IA32/Linux+Windows Register Usage
ECNU
%eax, %edx, %ecx
  Caller saves prior to call if values are used later
%eax
  also used to return integer value
%ebx, %esi, %edi
  Callee saves if wants to use them
%esp, %ebp
  special form of callee save
  Restored to original values upon exit from procedure
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
Caller-Save
Temporaries
Callee-Save
Temporaries
Special

## Slide 54: Today
ECNU
Switch statements
IA 32 Procedures
  Stack Structure
  Calling Conventions
  Illustrations of Recursion & Pointers

## Slide 55: Recursive Function
ECNU
/* Recursive popcount */
int pcount_r(unsigned x) {
if (x == 0)
return 0;
else return
(x & 1) + pcount_r(x >> 1);
}
Registers
  %eax, %edx used without first saving
  %ebx used, but saved at beginning & restored at end
pcount_r:
pushl %ebp
movl %esp, %ebp
pushl %ebx
subl $4, %esp
movl 8(%ebp), %ebx
movl $0, %eax
testl %ebx, %ebx
je .L3
movl %ebx, %eax
shrl %eax
movl %eax, (%esp)
call pcount_r
movl %ebx, %edx
andl $1, %edx
leal (%edx,%eax), %eax
.L3:
addl $4, %esp
popl %ebx
popl %ebp
ret

## Slide 56: Recursive Call #1
ECNU
/* Recursive popcount */
int pcount_r(unsigned x) {
if (x == 0)
return 0;
else return
(x & 1) + pcount_r(x >> 1);
}
Actions
  Save old value of %ebx on stack
  Allocate space for argument to recursive call
  Store x in %ebx
pcount_r:
pushl %ebp
movl %esp, %ebp
pushl %ebx
subl $4, %esp
movl 8(%ebp), %ebx
• • •
x
Rtn adr
Old %ebp
%ebp
•
•
•
%esp
Old %ebx
x
%ebx

## Slide 57: Recursive Call #2
ECNU
/* Recursive popcount */
int pcount_r(unsigned x) {
if (x == 0)
return 0;
else return
(x & 1) + pcount_r(x >> 1);
}
Actions
  If x == 0, return
    with %eax set to 0
• • •
movl $0, %eax
testl %ebx, %ebx
je .L3
• • •
.L3:
• • •
ret
x
%ebx

## Slide 58: Recursive Call #3
ECNU
/* Recursive popcount */
int pcount_r(unsigned x) {
if (x == 0)
return 0;
else return
(x & 1) + pcount_r(x >> 1);
}
Actions
  Store x >> 1 on stack
  Make recursive call
Effect
  %eax set to function result
  %ebx still has value of x
• • •
movl %ebx, %eax
shrl %eax
movl %eax, (%esp)
call pcount_r
• • •
Rtn adr
Old %ebp
%ebp
•
•
•
%esp
Old %ebx
x >> 1
x
%ebx

## Slide 59: Recursive Call #4
ECNU
/* Recursive popcount */
int pcount_r(unsigned x) {
if (x == 0)
return 0;
else return
(x & 1) + pcount_r(x >> 1);
}
Assume
  %eax holds value from recursive call
  %ebx holds x
Actions
  Compute (x & 1) + computed value
Effect
  %eax set to function result
• • •
movl %ebx, %edx
andl $1, %edx
leal (%edx,%eax), %eax
• • •
x
%ebx

## Slide 60: Recursive Call #5
ECNU
/* Recursive popcount */
int pcount_r(unsigned x) {
if (x == 0)
return 0;
else return
(x & 1) + pcount_r(x >> 1);
}
Actions
  Restore values of %ebx and %ebp
  Restore %esp
• • •
L3:
addl $4, %esp
popl %ebx
popl %ebp
ret
Rtn adr
Old %ebp
%ebp
•
•
•
%esp
Old %ebx
Old %ebx
%ebx
%ebp
•
•
•
%esp

## Slide 61: Observations About Recursion
ECNU
Handled Without Special Consideration
  Stack frames mean that each function call has private storage
    Saved registers & local variables
    Saved return pointer
  Register saving conventions prevent one function call from corrupting another’s data
  Stack discipline follows call / return pattern
    If P calls Q, then Q returns before P
    Last-In, First-Out
Also works for mutual recursion
  P calls Q; Q calls P

## Slide 62: Pointer Code
ECNU
/* Compute x + 3 */
int add3(int x) {
int localx = x;
incrk(&localx, 3);
return localx;
}
Generating Pointer
add3 creates pointer and passes it to incrk
/* Increment value by k */
void incrk(int *ip, int k) {
*ip += k;
}
Referencing Pointer

## Slide 63: Creating and Initializing Local Variable
ECNU
%esp
int add3(int x) {
int localx = x;
incrk(&localx, 3);
return localx;
}
Variable localx must be stored on stack
  Because: Need to create pointer to it
Compute pointer as -4(%ebp)
First part of add3
x
Rtn adr
Old %ebp
%ebp
0
4
8
-4
localx = x
Unused
-12
-8
-16
add3:
pushl %ebp
movl %esp, %ebp
subl $24, %esp # Alloc. 24 bytes
movl 8(%ebp), %eax
movl %eax, -4(%ebp) # Set localx to x
-20
-24

## Slide 64: Creating Pointer as Argument
ECNU
%esp
int add3(int x) {
int localx = x;
incrk(&localx, 3);
return localx;
}
Use leal instruction to compute address of localx
Middle part of add3
x
Rtn adr
Old %ebp
%ebp
0
4
8
-4
localx
Unused
-12
-8
-16
movl $3, 4(%esp) # 2nd arg = 3
leal -4(%ebp), %eax # &localx
movl %eax, (%esp) # 1st arg = &localx
call incrk
-20
-24
3
%esp+4

## Slide 65: Retrieving local variable
ECNU
%esp
int add3(int x) {
int localx = x;
incrk(&localx, 3);
return localx;
}
Retrieve localx from stack as return value
Final part of add3
x
Rtn adr
Old %ebp
%ebp
0
4
8
-4
localx
Unused
-12
-8
-16
movl -4(%ebp), %eax # Return val= localx
leave
ret
-20
-24

## Slide 66: IA 32 Procedure Summary
ECNU
Important Points
  Stack is the right data structure for procedure call / return
    If P calls Q, then Q returns before P
Recursion (& mutual recursion) handled by normal calling conventions
  Can safely store values in local stack frame and in callee-saved registers
  Put function arguments at top of stack
  Result return in %eax
Pointers are addresses of values
  On stack or global
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
Old %ebp
Arguments
Caller
Frame
%ebp
%esp

## Slide 67: Homeworks
ECNU
3.59,3.62,3.66